## Slide 1
Scenario
Input data and assumptions
literature review
experiments
Simulation outputs
Module
Air
Module
Surfaces
Module
Workers
Module
Food
sedimentation
Characteristics of SARS-CoV-2
Behaviours
Extrinsic parameters
Meat processing plant
Food contamination
Infected workers
transfers
exhalation
inhalation
Simulations
Comparison for model validation perspectives
Industrial & Epidemiological investigations
variants of concerns,
attack rates…
dimensions, ventilation, temperature, humidity…
mask wearing,
community activities…
Agent-Based Model
Surfaces contamination
Epidemiological data
Model outline
contamination
Notes: 1 minutes

## Slide 2
Office
Conveyor
Cutters
Cutters
Logistic
Logistic
Transverse
(manager, administrative…)
Arrival gate
Entry hall
Waste area
W.C.
Cutting room
Conveyor
Equipment
(packaging)
Cooling area
Transverse
(cleaning team)
Modelling the meat processing plant
Notes: 1min30

## Slide 3
Workers contamination
Air in the room
sedimentation of droplets on inert surfaces and food
Air flow
Ventilation system
Air renewal
Infectious workers
aerosolized droplets
(with/without infectious virions –
Several size classes)
Contamination of surfaces and meat cuts
coughing,
sneezing,
talking…
droplets projections
transfers between
inert surfaces and food portions
direct fall of
high-diameter droplets
Transmission of SARS-CoV-2 between different agents
Duration (days)
between infection states
newly
infected
infectious
symptomatic
asymptomatic
recovered
non
infectious
mask ?
contamination
inside the plant
air
epidemic situation prevalence
community activities
co-living, …
other contamination
sources
(“outside”)
inhaled doses ?
Notes: 1min30

## Slide 4
Sources de contamination
Contamination en dehors de l’atelier
situation épidémique régionale
Module Opérateurs
Transmission
au sein de l’atelier ?
Activités
en communauté

## Slide 5
Air in the room
sedimentation
Air flow rate
Air conditionner
% air renewal
mask
mask
different droplet size classes
aerosolized droplets
(with/without infectious virions)
Total number of droplets
inhaled by each worker
(end of the day)
Infectious workers
Susceptible worker(s)
Individual variability:
mask wearing, respiratory activities, symptoms development, …
direct fall of
high-diameter droplets
Notes: Port du masque (préférence / efficacité)
Paramètres associés à différentes actions des opérateurs : taux de respiration, concentration de gouttelettes émises en fonctions de l’activité  détail par SD

## Slide 6
Worker contamination
Air in the room
sedimentation of droplets on inert surfaces and food
Batterie
froide
Air flow
Air conditioning system
Air renewal
mask
mask
Infectious workers
Susceptible worker(s)
Individual variability: mask wearing, respiratory activities, symptoms development, emitted viral quantity, etc.
aerosolized droplets
(with/without infectious virions)
Food contamination
coughing, sneezing, talking, etc.
droplets projections
transfer from inert surfaces to food portions
direct fall of
high-diameter droplets
Surfaces contamination
Notes: Sédimentation sur surfaces/viandes
Transferts